RP2350-PICO2-XL
RP2350-PICO2-XXL
User Manual
Document 2.1 August 2025	www.olimex.com
# Introduction to RP2350-PICO2-XXL

RP2350-PICO2-XXL is a re-design of the popular “Raspberry Pi Pico 2” board with these improvements:

- RP2350B Dual Cortex-M33 or dual RISC-V @ 150MHz
- All 48 RP2350 GPIOs exposed to the user
- USB-C connector for data and powering – it allows more current to be supplied to the board
- DCDC power supply voltage regulator 3.3V 2A (3A peak)
- 2MB or 16MB flash memory versions (-XL and -XXL variants)
- Extra 8MB PSRAM in the -XXL variant
- Micro SD card connector in the -XXL variant
- BOOT and RESET buttons
- Four-layer board for better noise immunity and USB differential pair routing
- UEXT connector (pUEXT 1.0 mm step connector)
- Qwiic/Stemma connector
- Status LED
- Dimensions: (50 x 28)mm ~ (1.97 x 1.10)"

Notice
The two board variants RP2350-PICO2-XL and RP2350-PICO2-XXL share the same PCB and silksreen! The three differences between -XL and -XXL variants are that:
- the -XXL variant has PSRAM,the -XL variant – no PSRAM;
- the -XXL variant has micro SD card, the -XL variant – no micro SD card connector;
- the -XXL has 16MB of flash memory, the flash memory of the -XL variant is only 2MB.
# Order codes for RP2350-PICO2-XXL and accessories

RP2350-PICO2-XL	industrial grade RP2350-PICO2 board with 48 GPIOs exposed
RP2350-PICO2-XXL	includes everything in XL, bigger flash, extra 8MB PSRAM, and	extra microSD card
USB-CABLE-AM-USB3-C	high quality USB 3.0 cable with type C connector for power and	programming
pUEXT pack of cables	pack of 3pcs 200mm pUEXT cables
UEXT-MPQ	converter board from pUEXT to UEXT
UEXT-PQ	another converter board from pUEXT
# HARDWARE
## RP2350-PICO2-XXL layout

Top view for both -XL and -XXL
Power supply
USB-C
2MB or 16MB Flash
RP2350B
pUEXT
RST1 reset button
LED
Qwiic Stemma
Boot button

Bottom view for -XL variant:
Bottom view for -XXL variant:

Micro SD card
8MB PSRAM
## RP2350-PICO2-XXL GPIOs

POWER SUPPLY:

VBUS	+5V from, USB-C output
VDD_SYS	+5V may be output or input
if you want to use as input i.e. to feed power from external 5V to this line make sure	the board is not connected to USB!
when you use it as output i.e. you feed external electronics from it up to 1A @ 5V
+3.3V	output which can source up to 2A @ 3.3V
3V3_EN	input, when pulled to GND stops the 3.3V DCDC convertor

## RP2350-PICO2-XXL schematics

RP2350-PICO2-XXL schematics can be found at GitHub:

https://github.com/OLIMEX/RP2350-PICO2-XXL/tree/main/HARDWARE

## UEXT connector

UEXT connector stands for Universal EXTension connector and contains +3.3V, GND, I2C, SPI, UART signals.
UEXT connector can be in different shapes.
The original UEXT connector is 0.1” 2.54mm step boxed plastic connector. All signals are with 3.3V levels.

As the boards become smaller and smaller some smaller packages were introduced too beside the original UEXT connector:
- mUEXT is 1.27 mm step boxed header connector which is with same layout as UEXT;
- pUEXT is 1.0 mm single row connector (this is the connector used in RP2040-PICO30).
Olimex has developed number of MODULES with this connector. There are temperature, humidity, pressure, magnetic field, light sensors. Modules with LCDs, LED matrix, Relays, Bluetooth, Zigbee, WiFi, GSM, GPS, RFID, RTC, EKG, sensors and etc.

## pUEXT signals

## Qwiic/Stemma connector

## Micro SD card connector

In latest hardware revisions (B and newer) the SD card is connected in SPI data mode:

Notice that in hardware revision A the board was connected in 1-bit MMC data mode.
## PSRAM connection

## LED connection

# SOFTWARE

RP2350-PICO2-XXL uses same software as PICO2
- Raspberry PI SDK, header can be found at this GitHub link
- MicroPython SDK (note that to the current date RP2350B chip support is not implemented in MicroPython and the access of the GPIO30-47 in MicroPython is not implemented.
- CircuitPython from Adafruit – all 48 GPIOs are implemented.
Original production binaries can be found at the GitHub link here
# Document Revision History
Revision 2.1 August 2025
- Improved formatting
Revision 2.0 April 2025
- Added latest schematics
- Improved formatting
Revision 1.0 January 2025